## Slide 1
Pre-spud Meeting January 10, 2022
Blackspur HZ Leduc-WB 16-11-51-2W5
Surface: 14-3-51-2W5M
Horizon Drilling Rig # 43

## Slide 2: AGENDA
Introductions
HSE
Project Overview
Operations Summary
Invoicing

## Slide 3: GENERAL SAFETY
HSE
  Driving Safely (winter conditions)
  Covid-19
  Sign off on Orientations
  Blackspur ERP to be on location at all times
  Wearing PPE (zero tolerance)
  Hazard Identification and Mitigation
  All participate in pre job safety meetings
  Right to Refuse Work, Line of Fire & Material Handling (lifting); Slips, Trips and Falls, Clean Shaven
  Hiring service providers that are leaders in H&S
  Lead by Example

## Slide 4: COVID SAFETY
Limit entry into wellsite trailers
Paperwork & invoices to be done electronically
Mudman/Environmental Tech – email reports and call supervisor with results/recommendations. Limit entry to doghouse or trailers
Cementers/Pressure testers – safety meetings outside if possible.
Command Center – masks worn if 2 m social distance can not be met.
Ensure people that feel unwell do NOT arrive on site.
Screening to be done if someone falls ill on location and has been isolated.

## Slide 5: COVID SAFETY

## Slide 6: EXPECTATIONS
Pro active safety reporting
  Report incidents immediately to your supervisor
    Near Misses will be treated as “free learning opportunity”
    Spills > 1 liter must be reported
  Reports all suspected injuries before the end of your shift (strains, tweak etc)
We will be successful if:
  We communicate with each other and look out for each other. All services and Blackspur personnel are on the same team
  When conditions/scope changes, we stop, think and plan before acting.
  Identify hazards and take positive action to correct them.

## Slide 7: PROJECT CONTACTS (Blackspur)
Name |  | Position | Office | Cell | Email
Drilling: |  |  |  |  | 
Rae | Derek | Engineering & Operations (CVE) |  | 403.701.0899 | rae@codeco-vanoco.com
Bowen | Mike | Wellsite Supervisor |  | 403.348.9127 | mikebowen@hotmail.ca
Burton | Darren | Wellsite Supervisor |  | 780.518.7767 | dburtonconsulting@gmail.com
HSE: |  |  |  |  | 
Pippard | Dan | HS&E Manager (CVE) |  | 587.437.8858 | Pippard@codeco-vanoco.com
Operations: |  |  |  |  | 
Veale | Graham | VP Engineering |  | 403.809.6684 | gveale@blackspuroil.com
Stanford | Nick | Drilling Manager |  | 403-804-0296 | nstanford@blackspuroil.com
Geology: |  |  |  |  | 
LaFleur | Shawn | Operations Geologist |  | 403.700.3550 | slafleur@blackspuroil.com
BLACKSPUR 24 HOUR EMERGENCY PHONE NUMBER 1-855-585-0554 |  |  |  |  | 

## Slide 8: WELL DESIGN
Surface:
Hole size: 311 mm
Casing: 244.5 mm
Setting: 265 mKB
Mud: Gel Chem
Problems: Possible lost circulation, gravel & boulders, possible mud rings
Directional: Survey every 50 meters and keep deviation under 1.5 deg inc.
Intermediate:
Hole size: 222 mm
Casing: 177.8 mm
Setting: 1560 mMD (1363 mTVD)
Mud: Silicate Floc Water to 1100 mMD
        Silicate Polymer Mud from 1100 mMD to ICP
H2S: None anticipated
Problems: No significant problems
Directional: Kick off at the HZ KOP at 1013 mKB building angle at 5 deg per 30 m
        Until pump tangent at 70 degrees. After 30 m pump tagent, build at 6.6 degrees per 30 meters to ICP.
Main:
Hole size: 159 mm
Liner/Tie Back: 114.3 mm
Mud: Clayfree Polymer mud to FTD
H2S: None Anticipated
Problems: No significant problems
Directional: Drill out and hole inc at 90 degrees, azimuth per Plan 2

## Slide 9: OPERATIONS SUMMARY
Surface Hole:
  Spud with 311 mm DF519 PDC on directional BHA (1.50 degree ADJ 7/8 4.0 stage).
  Survey every 50 meters and maintain inclination under 1.5 deg.
  Sand and gravel potential on surface.
  Minor potential for losses & mud rings.
  Mud weight ALAP.
  Circulate clean, back ream out of the hole for casing.
  244.5 mm surface casing to be run and cemented to surface using 80% XS over gauge.
  Install 279.4 mm x 244.5 mm, 21 mPa casing bowl.

## Slide 10: OPERATIONS SUMMARY
Intermediate Hole:
  Gas detector rigged in & operational from surface drillout to FTD.
  Drill out with 222 mm GTD54MR on directional assembly (2.12 degree FXD 7/8 5.0 stage with MWD, GRWD & Jars)
  Use Silicate Floc water from SCP to 1100 mMD, then mud up to a Silicate Polymer mud system to ICP. Keep MW ALAP.
  At Final TD, circulate, wiper trip to SCP, circulate clean and POOH
  Run 177.8 mm, 34.2 kg/m, P-110, BTC casing, filling pipe every 10 stands
  Use 90% excess over gauge hole to cement intermediate section

## Slide 11: OPERATIONS SUMMARY
Main Hole:
  Drill out with 159 mm TKC63-B1 on 1.83 degree ADJ 6/7 lobe 8.0 stage directional assembly (with MWD, GRWD & Jars)
  Have Typhoon reamer one joint above the BHA, Jars and a ball drop agitator 700 meters above the BHA.
  Use Clayfree Polymer from drillout to Final TD. Keep weight ALAP.
  At Final TD, circulate, wiper trip to ICP, run back to bottom reaming any doglegs over 4 degrees, circulate clean and POOH
  Run 114.3 mm, 20.9 kg/m, P-110, GBCD Liner with two Interra toe sleeves, ~65 NCS multicycle sleeves and Packers Plus liner hanger, filling pipe every 10 stands
  Liner top 40 m inside 177.8 mm casing
  Use 60% excess over gauge hole to cement liner
  Run 114.3 mm, 20.9 kg/m, P-110, BTC tieback string from TOL to surface

## Slide 12: INVOICING
FIELD TICKETS
Must be approved by the Wellsite Supervisor
Must have the company name and location (UWI) clearly identified
Must have the AFE number on them
Must have the sub-code as well
Any corrections to the field tickets must be initialed by the Wellsite Supervisor
INVOICES
ALL INVOICES MUST BE SUBMITTED to Blackspur Oil Corp via CORTEX
ALL INVOICES MUST HAVE SIGNED FIELD TICKETS ATTACHED TO THE INVOICES

## Slide 13: QUESTIONS
OPEN FORUM